## Slide 1: ECEN 5623 Real-Time Embedded Systems Team #13 Ayswariya Kannan, Kiran Jojare
Real-time Stop Sign Detection For Vehicles

## Slide 2: Presentation Roadmap
Introduction
System Block Diagram
Capability Requirements
Real Time Requirements
Performance Requirements - WCET
Service Set Feasibility and Safety Analysis
System Response Timeline Diagram
Flowchart & DFD
Proof-of-Concept Analysis
Verification & Validation Plans
Summary

## Slide 3: Introduction
The primary objective is to prototype a real-time embedded system that serves as a sign detection bot, which will be able to detect and respond to STOP signs, enhancing safety and situational awareness in intelligent transportation systems.
Using the OpenCV library and the camera module on the Jetson Nano, we employ image processing techniques to detect traffic signs by leveraging Haar Cascade classifiers.
We are leveraging the FreeRTOS kernel on the TIVA C123GX for efficient multitasking and prioritization maintaining real-time requirements.

## Slide 4: System Block Diagram
6V

## Slide 5: Capability Requirements
High-Performance Traffic Sign Detection: The camera interfaced with an NVIDIA Jetson Nano for detecting STOP signs, operating at 640 x 480 resolution, optimizing image quality and computational demand.
Reliable and Fast Data Communication: The NVIDIA Jetson Nano reliably communicates processed traffic sign data to the TIVA C123G microcontroller using UART at a baud rate of 115200 bps.
Precise and Responsive Motor Actuation: Initiating motor actuation within 10 msec of receiving the command is crucial to ensure the vehicle's safe and efficient response to STOP sign.
Status Indication through LED Notification: The LED should illuminate within 250 msec of traffic sign detection and motor action execution, providing prompt diagnostics feedback to the vehicle operator.

## Slide 6: Real-Time Requirements
For traffic sign detection to work, we need the braking system to activate performing better than the human reaction time, as per the research paper the average brake reaction for males is 0.50 seconds and for females is 0.53 seconds. Thus, we have kept the total system response timeline as 500 msec.
As per the research done, we have the deadline for the camera service task as 200 msec.
According to the research paper, we have a deadline for the motor control task for the right and left motor as 10 msec.
LED service is a lower-priority task with a deadline of 250 msec.

## Slide 7: Real-Time Requirements Contd..
We have four services:
  S1: Camera Data Reception from Jetson Nano
  S2: Right Motor Control
  S3: Left Motor Control
  S4: Diagnostic LED Control
We have taken period same as the deadline for the Rate monotonic scheduling policy, shown in the table below.
D1+D2+D3+D4 = 470 msec < 500 msec (system response deadline)
Services | Task | Deadline(ms) | Time period(ms) | Priority(ms)
S1 | Camera Data Reception from Jetson Nano | 200 | 200 | 2 (Medium)
S2 | Right Motor Control | 10 | 10 | 1 (Highest)
S3 | Left Motor Control | 10 | 10 | 1 ((Highest))
S4 | LED Control | 250 | 250 | 3 (Lowest)

## Slide 8: Performance Requirements
According to the research paper referred, the WCET for camera service is 327 msec considering the Quad-core ARM® Cortex®-A57 MPCore processor
Motor control service has a WCET requirement of 3 msec according to the research paper
Utilizing the clock frequency of the TIVA board (80 MHz), GPIO pins can be configured with a reduced instruction set and may require up to 2 milliseconds to complete. WCET requirement for LED control service = 2 msec

## Slide 9: Service Set Feasibility and Safety Analysis
WCET: Expected Ci vs Actual
TIVA services have almost similar WCET values to predicted
For Service S1: WCET is 69 msec performed better than expected
For Service S2 &S3: WCET actual is 3 msec matching the predicted values.
For Service S4: It is 1 msec better than the predicted.
Services | Task | WCET Expected (ms) | WCET Actual (ms) | Deadline(ms) | Time period(ms) | Priority(ms)
S1 | Camera Data Reception from Jetson Nano | 327 | 69 | 200 | 200 | 2 (Medium)
S2 | Right Motor Control | 3 | 3 | 10 | 10 | 1 (Highest)
S3 | Left Motor Control | 3 | 3 | 10 | 10 | 1 ((Highest))
S4 | LED Control | 2 | 1 | 250 | 250 | 3 (Lowest)

## Slide 10: Cheddar Analysis for Worst-Case and Simulation
According to Cheddar Analysis , Total utilization with the actual WCET= 94.9%
We can’t prove feasibility with RM LUB Test as it is above RM LUB 75.683%.
Based on Necessary & Sufficient test, it can be seen task set is schedulable
Safety Margin is 5.1%
Safety : No deadline missed

## Slide 11: Scheduling Point and Completion Time Test

## Slide 12: System Response Timeline
Input Latency
S1 Execution
Context Switch
S4 Execution
Context Switch
S2 Execution
Context Switch
S3 execution
O/p Latency
Event Sensed
200 msec
10 msec
10 msec
250 msec
Actuation
Deadline : 500 msec

## Slide 13: SA/SD State Machine DESIGN

## Slide 14: Control Flow Diagram(CFD)

## Slide 15: Data Flow Diagram

## Slide 16: Proof-of-Concept Analysis
Platform Resources
  Jetson Nano – Linux OS, Open CV4
  TIVA C123GX –freeRTOS Kernel
  L293D Motor driver
Key Prototype Implementation :
  Camera service in Jetson Nano using openCV4 with Haar cascade classifier
  UART Communication between Jetson Nano and TIVA
  Motor Driver Firmware using PWM over TIVA
  Sequencer Implemented using Timer Interrupt
  Semaphores for synchronization between services and data shared between UART interrupt and services.

## Slide 17: Hardware Prototype

## Slide 18: Proof of Concept Demo

## Slide 19: Time-stamp Tracing of Key Services
Time stamps of camera service in Jetson Nano

## Slide 20: Time-stamp Tracing of Key Services Contd..
WCET values from time stamp In TIVA C123G
Start and stop timestamps for services on TIVA C123G

## Slide 21: Verification & Validation Plans
Software Engineering: A Practitioner’s Approach, 8/e (McGraw-Hill, 2014) copyright 2014 by Roger Pressman
Requirements Modelling
Acceptance Testing
Architectural Design
Component Design
Code Gen
System Testing
Integration testing
Unit Testing
Executable software
Defined functional requirements including stop sign detection using OpenCV on Jetson Nano and motor control via UART communication with TIVA123.
Designed the system architecture to integrate two microcontrollers (TIVA123 and Jetson Nano)
Detailed component specifications for the software modules handling UART data reception, motor control logic, and onboard LED diagnostics.
Developed the code for each component in C, ensuring compatibility with the RTOS environment on TIVA123 and OpenCV on Jetson Nano
Performed isolated tests for individual modules such as UART communication, motor control functions, and LED diagnostics to ensure functional integrity
Tested the integration of all modules to verify data flow from the Jetson Nano to TIVA123 and the correct motor responses based on the received commands.
Evaluated the entire system's performance, focusing on real-time task scheduling adherence and response accuracy to stop sign detection.
Conducted final testing to ensure the system meets the initial project requirements and functions correctly under intended operating conditions.

## Slide 22: Summary
Developed a cohesive system combining Jetson for image processing and TIVA for motor control, utilizing FreeRTOS for task management.
Achieved precise real-time detection and control, highlighting the critical role of service deadlines in real-time systems.
Integrated the camera module with the Jetson and established UART communication with TIVA. Implemented motor control using an L293D motor driver, ensuring the functionality sequence was maintained
Scheduled and executed all services within the defined timelines, effectively meeting all system deadlines.
Enhanced understanding of embedded systems and real-time applications, with significant challenges overcome in system integration and UART communication stability.

## Slide 23: Thank You Prof Tim Nilesh, Viraj and Rishi Fellow classmates
Questions?